## Slide 1
TEMA X. DISTRIBUCIÓN DE HIDRÓGENO.
TIPOLOGÍA Y EQUIPOS EXISTENTES EN EL MERCADO.
Tema III Transporte y distribución

## Slide 2: AGENDA
Introduction.
Compressed gas cylinders or Cryogenic liquid tankers.
Pipelines.
Blending with natural gas.
Tema III Transporte y distribución

## Slide 3: AGENDA
Introduction.
Compressed gas cylinders or Cryogenic liquid tankers.
Pipelines.
Blending with natural gas.
Tema III Transporte y distribución

## Slide 4: Introduction
Tema III Transporte y distribución
Hydrogen is easy to transport easy in long distance and can be transported in different formats.
Today, the transport of compressed gaseous or liquid hydrogen by lorry and of compressed gaseous hydrogen by pipeline to selected locations are the main transport options used.
The most common hydrogen transportation means, covering the needs of the different hydrogen markets, are:
Compressed gas cylinders or Cryogenic liquid tankers.
Pilelines (stell and plastics).
Blending with natural gas.

## Slide 5: AGENDA
Introduction.
Compressed gas cylinders or Cryogenic liquid tankers.
Pipelines.
Blending with natural gas.
Tema III Transporte y distribución

## Slide 6: Compressed gas cylinders or Cryogenic liquid tankers. .
Tema III Transporte y distribución

## Slide 7: Compressed gas cylinders or Cryogenic liquid tankers. .
Tema III Transporte y distribución

## Slide 8: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 9: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 10: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 11: Compressed gas cylinders.
Tema III Transporte y distribución
Gaseous hydrogen can be transported in small to medium quantities in compressed gas containers by lorry. For transporting larger volumes, several pressurized gas cylinders or tubes are bundled together on so-called CGH2 tube trailers. The large tubes are bundled together inside a protective frame.
The tubes are usually made of steel and have a high net weight. This can lead to mass-related transport restrictions. The newest pressurized storage systems use lighter composite storage containers for lorry transport.
The low density of hydrogen also has an impact on its transport: under standard conditions (1.013 bar and 0°C), hydrogen has a density of 0.0899 kg per cubic meter (m3), also called normal cubic meter (Nm3).
If hydrogen is compressed to 200 bar, the density under standard conditions increases to 15.6 kg hydrogen per cubic meter, and at 500 bar it would reach 33 kg H2/m3.

## Slide 12: Compressed gas cylinders.
Tema III Transporte y distribución
A tube trailer cannot store compressed gas as compactly as a tanker for liquid fuels (petrol or diesel fuel). This means that the available tank volume for hydrogen per tanker is lower. Single tube trailers carry approximately 500 kg of hydrogen, depending on the pressure and container material.
The largest tank volumes for gaseous hydrogen transport are currently 26 cubic meters. Taking account of the low hydrogen density factor at 500 bar, this results in a load of around 1,100 kg hydrogen per lorry. This figure extrapolates to approximately 12,000 normal cubic meters of hydrogen. At 250 bar both the weight of hydrogen and its transport volume in Nm3 would be roughly halved. The ambition is the development of a 700 bar tube trailers (c. 1,500kg) in the coming years.

## Slide 13: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 14: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 15: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 16: Compressed gas cylinders.
Tema III Transporte y distribución

## Slide 17: Cryogenic liquid tankers.
Tema III Transporte y distribución
LH2-sized tank cars have a capacity of 7,711 kg. The pressure within the tank is typically 1.7 bara or lower and the temperature is usually below −252.87 °C. The boil-off rate is around 0.3–0.6% per day.

## Slide 18: Cryogenic liquid tankers.
Tema III Transporte y distribución
As an alternative, hydrogen can be transported in liquid form in lorries or other means of transport. In comparison to pressure gas vessels, more hydrogen can be carried with an LH2 trailer, as the density of liquid hydrogen is higher than that of gaseous hydrogen.
Since the density even of liquid hydrogen is well below that of liquid fuels, at approx. 800 kg/m3, in this case too only relatively moderate masses of hydrogen are transported. At a density of 70.8 kg/m3 , around 3,500 kg of liquid hydrogen or almost 40,000 Nm3 can be carried at a loading volume of 50 m3.
Over longer distances it is usually more cost-effective to transport hydrogen in liquid form, since a liquid hydrogen tank can hold substantially more hydrogen than a pressurized gas tank. For the purposes of liquid transport the hydrogen is loaded into insulated cryogenic tanks. LH2 trailers have a range of approximately 4,000 km. Over the journey time the cryogenic hydrogen heats up, causing the pressure in the container to rise.
Similarly, to lorry transport, LH2 can also be transported by ship or by rail, provided that suitable waterways, railway lines and loading terminals are available.

## Slide 19: Cryogenic liquid tankers.
Tema III Transporte y distribución
H2 in liquid form is the most conventional means of transporting bulk hydrogen on the road. The H2 is stored at -253°C in super-insulated ‘cryogenic’ tankers. However, liquefaction is energy intensive and storage/transport of the LH2 results in heat ingress and losses due to evaporation.
“Boil-off” losses can be reduced by improved insulation concepts or, as illustrated by NASA, by an integrated refrigeration and storage system. It should be noted that most of the boil-off happens during transfer phase (Storage to Trailer, Trailer to local storage), far above the vaporization inside storage tanks.

## Slide 20: Cryogenic liquid tankers.
Tema III Transporte y distribución

## Slide 21: Cryogenic liquid tankers.
Tema III Transporte y distribución

## Slide 22: AGENDA
Introduction.
Compressed gas cylinders or Cryogenic liquid tankers.
Pipelines.
Blending with natural gas.
Tema III Transporte y distribución

## Slide 23: Pipelines.
Tema III Transporte y distribución
A pipeline network would be the best option for the comprehensive and largescale use of hydrogen as an energy source. However, pipelines require high levels of initial investment, which may pay off, but only with correspondingly large volumes of hydrogen.
Nevertheless, one possibility for developing pipeline networks for hydrogen distribution is local or regional networks, known as micro-networks. These could subsequently be combined into transregional networks.
Worldwide there are already (2016) more than 4,500 km of hydrogen pipelines in total, the vast majority of which are operated by hydrogen producers (HyARC 2017).
The longest pipelines are operated in the USA, in the states of Louisiana and Texas, followed by Belgium and Germany.

## Slide 24: Pipelines.
Tema III Transporte y distribución
Pipelines for delivering large volumes of hydrogen over land pipelines are a leading option. In Europe there is already >1000 km dedicated hydrogen pipelines serving the industry. This network should be expanded by new build pure H2 pipelines.
Development of new high strength materials resistant to H2 cracking can increase the pressure and capacity of H2 pipelines, decreasing the cost of transportation.

## Slide 25: Pipelines.
Tema III Transporte y distribución

## Slide 26: Pipelines.
Tema III Transporte y distribución

## Slide 27: Pipelines.
Tema III Transporte y distribución

## Slide 28: Pipelines.
Tema III Transporte y distribución
SoluForce has developed a spoolable Reinforced Thermoplastic industrial Piping system (RTP, also known as FCP) for hydrogen applications. The SoluForce FCP has been certified for hydrogen applications up to 42 bar of operating pressure. Unique in the world of hydrogen transport and a global first. This significant milestone has a major impact on the feasibility of hydrogen, and is a new step towards a sustainable energy mix.
Benefits of the SoluForce Hydrogen Tight (H2T)
Certified for hydrogen applications of up to MOP 42 bar/ 609 psi, at maximum operating temperature of 65°C for up to 50 years.
Based on proven and existing technologies.
The only Flexible Composite Pipe for hydrogen applications available.
Quick and easy to install.

## Slide 29: Pipelines.
Tema III Transporte y distribución
Main advantages
  Operating pressure of 42 bar.
  No permeation.
  Fully certified.
  Non-metallic fitting system.
  Main advantages compared to steel
    No hydrogen embrittlement
    No corrosion
    Fully flexible
    Easy and quick to install
    Reusable
    Maintenance-free
    Design life of up to 50 years
    400-metre lengths per coil
    Extremely robust
4 inches and 6 inches availability.
  80 €/m for 4 inches pipe.
  100 €/m for 6 inches pipe.

## Slide 30: AGENDA
Introduction.
Compressed gas cylinders or Cryogenic liquid tankers.
Pipelines.
Blending with natural gas.
Tema III Transporte y distribución

## Slide 31: Blending with natural gas.
Tema III Transporte y distribución
Blending hydrogen into natural gas pipeline networks has also been proposed as a means of delivering pure hydrogen to markets, using separation and purification technologies downstream to extract hydrogen from the natural gas blend close to the point of end use.
As a hydrogen delivery method, blending can defray the cost of building dedicated hydrogen pipelines or other costly delivery infrastructure during the early market development phase.
Until well into the 20th century, hydrogen-rich town gas or coke-oven gas with a hydrogen content above 50 vol % was distributed to households in Germany, the USA and England, for example, via gas pipelines – although not over long distances, for which as yet no experience is availability.
Infrastructure elements that were installed at the time, such as pipelines, gas installations, seals, gas appliances etc., were designed for the hydrogen-rich gas and were later modified with the switch to natural gas.
Many countries have looked at adding hydrogen into the existing natural gas networks. For the USA, it would be possible to introduce amounts from 5 vol% to 15 vol% hydrogen without substantial negative impact on end users or the pipeline infrastructure.

## Slide 32: Blending with natural gas.
Tema III Transporte y distribución
At the same time, the larger additions of hydrogen would in some cases require expensive conversions of appliances. In Germany this limit has been set somewhat lower, at up to 10 vol%. In principle, gas at concentrations of up to 10 vol% hydrogen can be transported in the existing natural gas network without the risk of damage to gas installations, distribution infrastructure, etc.
However, a number of components have been listed that are still considered to be critical and to be generally unsuitable for operation with these hydrogen concentrations. For CNG vehicles, the currently authorized limit value for the proportion of hydrogen used is only 2 vol%, depending on the materials built in.
It can be assumed that many of the gas transport networks, distribution lines and storage facilities that were operated in the past are still in use today. In Leeds (UK), for instance, the possibility has been explored of converting the existing natural gas network in the region (used primarily for municipal heating supply) entirely to hydrogen. Given their length, the large gas networks in many industrial countries could store considerable amounts of hydrogen.

## Slide 33: Blending with natural gas.
Tema III Transporte y distribución

## Slide 34: Blending with natural gas.
Tema III Transporte y distribución

## Slide 35: Blending with natural gas.
Tema III Transporte y distribución

## Slide 36: ¡¡MUCHAS GRACIAS POR SU ATENCIÓN!!
ÍNDICE